# Text boxes

If you need new parts here's the numbers

6781550 Cap

6781549 Clip

Push in the middle of the clip and these will drop out.

If you need new ones part number is

6483390 Clip

You only need to do the drivers side as you can just lift it out of the way a bit.

This is the de-ice switch

Remove this.

This is the re-circ actuator

vacuum reservoir.

When you have moved the Re-Circ actuator reservoir out of the way you will be able to undo the 2 screws holding the de-ice switch.

This will give you plenty of access to the wires.

Connect the two wires from the AC Mod to the 2 black wires that come out of the de-ice switch. This is the thermistor wires and they go into the evap unit.

You can either scotchlock these or cut and solder them. It doesn’t matter which way round they go.

Pass the wires through the same hole used for the buzzer on global closing device or use the place pete mentioned on the website.